TOWARDS CORRECT-BY-CONSTRUCTION SDN
Leonid Ryzhyk Nikolaj Bjorner Marco Canini Jean-Baptiste Jeannin Nina Narodytska
Cole Schlesinger Douglas Terry George Varghese
22 August 2016

---
INTRODUCTION
- Cocoon is a
  - high-level SDN programming language
  - verification tool
  - SDN programming methodology
- … based on the principle of correctness by construction

---
COCOON IN A NUTSHELL
Traditional SDN Verification Workflow
Design
Implement
Run on the
controller
Verify generated
network configuration
SDN verification with Cocoon
refine
refine
refine
spec
implementation
Correct by construction

---
EXAMPLE: CAMPUS NETWORK
[Sung et al. Towards Systematic Design of Enterprise Networks]
L2 segment
Router
VLAN Gateway
Switch

---
INTER-VLAN ROUTING: HOP1

---
INTER-VLAN ROUTING: HOP2

---
INTER-VLAN ROUTING: HOP3
This is messy:
Large, ad hoc topology
L2/L3 routing are mixed up
Complex distributed security policies
Typical bugs:
ACL distribution
Routing loops
Black holes
Let’s try to untangle this design …

---
STEP 1: HIGH-LEVEL SPECIFICATION

---
STEP 2: DISTRIBUTED ACLs

---
STEP 2: DISTRIBUTED ACLs
Gateways
Assumption: acl() ≡ aclOut() Λ aclIn()

---
STEP 3: L3 ROUTING

---
STEP 3: L3 ROUTING
Routers
Assumption: L3NextHop(pkt)* = Gateway(pkt)

---
STEP 4: L2 SWITCHING

---
STEP 4: L2 SWITCHING

---
STEP 4: L2 SWITCHING
L2 switches
Assumption: L2NextHop(pkt)* = L3NextHop(pkt)

---
STEP 4: L2 SWITCHING
L2NextHop(pkt.vlan=0)
L2NextHop(pkt.vlan=green)
L2NextHop(pkt.vlan=red)
L2NextHop(pkt.vlan=blue)

---
SEPARATION OF CONCERNS
High-level spec
Distributed access control
L3 routing
L2 switching

---
WOULDN’T IT BE GREAT TO BUILD SDNs
THIS WAY?
With Cocoon, you can!
Language support for refinement-based programming
Automatic compositional verification
P4 and OpenFlow (via NetKAT) backends

---
PARAMETERIZED SPECIFICATIONS
- Parameterized specifications
  - Spec may contain undefined functions, e.g., acl(), l2NextHop(), l3NextHop()
  - Verification relies on assumptions
  - These functions are defined when the network design is instantiated
  - They can also change at runtime, e.g., in response to link failures
  - Assumptions are validated when concrete definitions are provided (statically or at runtime)

---
CASE STUDIES
Campus network
[Sung et al. Towards Systematic Design of Enterprise Networks]
F10
[Liu et al. F10: A Fault-Tolerant Engineered Network]
B4-style WAN
[Jain et al. B4: Experience with a Globally-Deployed Software Defined WAN]
iSDX (Software-defined Internet Exchange)
[Gupta et al. An Industrial-Scale Software Defined Internet Exchange Point]
NSX-style network virtualization framework
[Koponen et al. Network Virtualization in Multi-tenant Datacenters]
Stag (source-based routing + security labels for fat-tree topology)

---
PERFORMANCE
- All case studies verified in ~10 sec,
  - Compositional verification (1 refinement at a time)
  - Parameterized verification amplifies the power of symbolic reasoning
- No direct comparison (yet) with existing tools like NetKAT, HSA, but expect them to slow down for larger topologies

---
COCOON VS TRADITIONAL NETWORK VERIFICATION
HSA/
NetKAT/
...
Correctness spec

---
COCOON VS TRADITIONAL NETWORK VERIFICATION
Traditional	Cocoon
Obtaining correctness specification
Dedicated specs developed for verification purposes	Correctness spec developed during the network design process
Correctness guarantees enforced by verification
Check for specific defects: reachability, isolation, loop-freedom	Functional equivalence
Verification time
Runtime verification: when a new configuration is installed	Static verification (only assumptions are validated at runtime)
Debugging support
Little help in understanding the cause of the bug	Bugs are localized to a specific refinement and network component

---
CONCLUSIONS
- Correct-by-construction SDN via iterative refinement:
  - Enforces modular design
  - Enables strong static correctness guarantees
  - Scales to complex realistic networks

---
EXAMPLE ASSUMPTION
assume (hid_t sid, vid_t vid, MAC dst)
   (l2distance(sid, vid, dst) > 1) =>
   l2distance(link(sid, l2NextHop(sid, vid, dst)), dst)
    == (l2distance(sid, vid, dst) - 1)