Correct-by-Construction
Networking
Leonid Ryzhyk
(joint work with Cole Schlesinger and Jean-Baptiste Jeannin)
March 23, 2016

---
Problem statement
- Context: complex dynamic networks
  - Primary use case: cellular core
  - Datacenter networking
- Challenge 1: Programming abstractions
- Challenge 2: Controller verification

---
Problem statement
What are the right abstractions for the Northbound interface?
Easy to use
Easy to ensure correctness (assuming compiler is correct)
Routing, FT, QoS hardwired in the compiler
SDN app
SDN app
Abstraction
SDN app
Policy languages
(FatTire, FlowTags, FML, E2)
Northbound
interface
SDN controller
The user is in control
Network programming is hard and error-prone
Scalable verification is hard
Southbound
interface
(OpenFlow)
Modular flowtable languages
(NetKAT, Pyretic)
Flowtable languages
(OpenFlow, P4)
Flexibility

---
Meanwhile in parallel universe...
- The network operator defines the policy function and the network topology
- Control and data plane logic is generated automatically
P: Flow → Service type
Network controller
Routing
Failure recovery
QoS, load balancing

---
Meanwhile in parallel universe...
- This requires a scalable near-optimal synthesis algorithm
- Such an algorithm does not exist
- Current tools employ a fixed set of tricks, e.g.,
  - Shortest path routing
  - Generic algorithm to deal with N link failures (FatTire)
  - Generic NFV protocol (E2, CoMB)
- We are stuck with arbitrary choices enforced by the compiler
P: Flow → Service type
Network controller
Routing
Failure recovery
QoS
Elasticity
Load balancing

---
Correct-by-construction networking
Spec0: Network policy
refinement
refinement
Spec1
Spec2
SpecN
- Refinements deal with network topology, routing, fault tolerance, load balancing, etc.
- Each refinement focuses on a fragment of the network
- Each refinement is simple enough to verify automatically
- The final specification describes each network component in detail and can be compiled directly into an SDN controller
- Correctness of each refinement guarantees that the final spec satisfies the high-level policy

---
Case study: B4-style WAN routing [1]
Site 0
Site 1
tunnel: SiteId → SiteId → Tag → TunnelId
nexthop: TunnelId → SiteId → PortNum
Internet
WAN switch
WAN switch
Tunnel
Site 2
WAN switch
[1] Jain et al. B4: Experience with a Globally-Deployed Software Defined WAN

---
Spec0: Network policy
Key range
Key
Role
(* true: host with the given IP exists *)
function ihost(IP4 addr): bool
function dst(Packet p): IP4
role HostOut[IP4 addr, uint<8> port] | ihost(addr) and port==8'd0 =
    if ihost(dst(pkt)) then
        send HostIn[dst(pkt), 8'd0]
role HostIn[IP4 addr, uint<8> port] | ihost(addr) and port==8'd0 =
    filter false
HostOut
HostIn

---
Spec1: Tunnel-based WAN routing
refine HostOut {
    function hostSite(IP4 addr): SiteId
    function tunnel(SiteId src, SiteId dst, Packet p): TunnelId
    function nexthop(TunnelId tun, SiteId site): uint<8>
    assume(SiteId src, SiteId dst, Packet p, TunnelId tid, SiteId next)
       (not (tid == tunnel(src, dst, p) and next == wanLink(src, nexthop(tid, src)).site)) or
       (wpConnected(src,nexthop(tid,src)) and
        (next == dst or
        wpConnected(next,nexthop(tid,next)) and wanLink(next,nexthop(tid,next)).site==dst))
    role HostOut[IP4 addr, uint<8> port] | ihost(addr) and port == 8'd0 =
        if hostSite(dst(pkt)) == hostSite(addr) then {
        if ihost(dst(pkt)) then
        send HostIn[dst(pkt), 8'd0]
        } else
        send WANSwitchLIn[hostSite(addr), 8'd0]
    role WANSwitchLIn[SiteId site, uint<8> port] | isite(site) and port == 8'd0 =
        pkt.vlan.valid := true;
        pkt.vlan.tag := tunnel(site, hostSite(dst(pkt)), pkt);
        send WANSwitchGOut[site, nexthop(tunnel(site, hostSite(dst(pkt)), pkt), site)]
    role WANSwitchLOut[SiteId site, uint<8> port] | isite(site) and port == 8'd0 =
        if ihost(dst(pkt)) and hostSite(dst(pkt)) == site then
        send HostIn[dst(pkt), 8'd0]
    role WANSwitchGOut[SiteId site, uint<8> port] | iwanPort(site, port) =
        if (wpConnected(site,port)) then
        send WANSwitchGIn[wanLink(site,port).site, wanLink(site,port).port]
    role WANSwitchGIn[SiteId site, uint<8> port] | iwanPort(site, port) =
        if (hostSite(dst(pkt)) == site) then
        if ihost(dst(pkt)) then
        send WANSwitchLOut[site,8'd0]
        else
        send WANSwitchGOut[site, nexthop(pkt.vlan.tag,site)]
}
Site 0
Site 1
Internet
WAN switch
WAN switch
Site 2
WAN switch

---
Spec2: Introducing local fabric
Site 0
Site 1
Internet
WAN switch
WAN switch
Site 2
WAN switch

---
Spec3,4: Fat-tree local routing[1]
Core
Pods
[1] Al-Fares, Loukissas, Vahdat. A Scalable, Commodity Data Center Network Architecture

---
Runtime reconfiguration
- Formalize runtime configuration as functions:
  - tunnel(), nexthop()
- Also, formalize failures using functions:
  - linkUp(), hostUp()
- Formalize important invariants that must hold in any configuration as assumptions
- Prove correctness using assumptions
- At runtime, configuration is set by user-supplied policies
  - The generated controller checks configuration against invariants before installing it.

---
Invariants
refine HostOut {
    function hostSite(IP4 addr): SiteId
    function tunnel(SiteId src, SiteId dst, Packet p): TunnelId
    function nexthop(TunnelId tun, SiteId site): uint<8>
    assume(SiteId src, SiteId dst, Packet p, TunnelId tid, SiteId next)
       (not (tid == tunnel(src, dst, p) and next == wanLink(src, nexthop(tid, src)).site)) or
       (wpConnected(src,nexthop(tid,src)) and
        (next == dst or
        wpConnected(next,nexthop(tid,next)) and wanLink(next,nexthop(tid,next)).site==dst))
    role HostOut[IP4 addr, uint<8> port] | ihost(addr) and port == 8'd0 =
        if hostSite(dst(pkt)) == hostSite(addr) then {
        if ihost(dst(pkt)) then
        send HostIn[dst(pkt), 8'd0]
        } else
        send WANSwitchLIn[hostSite(addr), 8'd0]
    role WANSwitchLIn[SiteId site, uint<8> port] | isite(site) and port == 8'd0 =
        pkt.vlan.valid := true;
        pkt.vlan.tag := tunnel(site, hostSite(dst(pkt)), pkt);
        send WANSwitchGOut[site, nexthop(tunnel(site, hostSite(dst(pkt)), pkt), site)]
    role WANSwitchLOut[SiteId site, uint<8> port] | isite(site) and port == 8'd0 =
        if ihost(dst(pkt)) and hostSite(dst(pkt)) == site then
        send HostIn[dst(pkt), 8'd0]
    role WANSwitchGOut[SiteId site, uint<8> port] | iwanPort(site, port) =
        if (wpConnected(site,port)) then
        send WANSwitchGIn[wanLink(site,port).site, wanLink(site,port).port]
    role WANSwitchGIn[SiteId site, uint<8> port] | iwanPort(site, port) =
        if (hostSite(dst(pkt)) == site) then
        if ihost(dst(pkt)) then
        send WANSwitchLOut[site,8'd0]
        else
        send WANSwitchGOut[site, nexthop(pkt.vlan.tag,site)]
}
Site 0
Site 1
Runtime
configuration
Internet
WAN switch
WAN switch
Invariant
Site 2
WAN switch

---
Tool architecture
Runtime
policy
Configuration
tunnel()
nexthop()
Checks
invariants
SDN controller
SpecN
SpecN
SpecN
Flow table
updates
Topology

---
Demo