Correct-by-Construction
Networking
March 9, 2016

---
Contents
Contents
5G and systems research challenges
The dependability challenge
Proposal: correct-by-construction networking
Demo
II
III
Ⅳ
Ⅰ

---
Heading
5G network overview
Internet
Middlebox types:
NAT
IDS
Firewalls
Audio/video transcoders
WAN optimizers
Caches (HTTP, Youtube, Netflix,...)
M3
M3
M3
M3
M2
M2
Data center
M1
M1
M1
Base stations
UE

---
Research challenges
Performance
  - Scalability
  - Latency
  - QoS
- Dependability
  - Correctness
  - Fault tolerance
- Monitoring
  - Real-time analytics
  - Offline analytics
- ...

---
The scalability challenge
Network policy:
P: Flow → Service type
Network controller
C: Service type → Route
Example:
P(Voice)=M1,M2,M3;delay<=5ms
C(M1,M2,M3;5ms)=M13,M22,M32
M3
M3
M3
M3
M2
M2
M1
M1
M1

---
The scalability challenge
Millions of routes
Easy to run out of switch TCAM
Millions of new flows/s
Continuous reconfiguration
SDN controller becomes a bottleneck
M3
M3
M3
M3
Extensive literature on this topic
SoftCell
E2
CoMB
...
M2
M2
M1
M1
M1

---
Research challenges
Performance
  - Scalability
  - Latency
  - QoS
- Dependability
  - Correctness
  - Fault tolerance
- Monitoring
  - Real-time analytics
  - Offline analytics
- ...

---
The dependability challenge
- Transition to SDN+NFV requires complete re-design of the core network
  - Before: specialized network appliances
  - After: commodity servers and switches
- Increased complexity
  - Decentralization
  - Increased likelihood of component failure
- With equipment manufacturers out of the picture, network operators are in charge of managing the entire hardware/software stack
- Uncertainty is a real roadblock to the 5G transition

---
Thank You!
Proposal:
Correct by Construction Networking

---
A strawman solution
- The network operator defines the policy function and the network topology
- Control and data plane logic is generated automatically
P: Flow → Service type
Network controller
Routing
Failure recovery
QoS, load balancing

---
A strawman solution
- This requires a scalable near-optimal synthesis algorithm
- Such an algorithm does not exist
- Current tools employ a fixed set of tricks, e.g.,
  - Shortest path routing
  - Generic algorithm to deal with N link failures (FatTire)
  - Generic NFV protocol (E2, CoMB)
- We are stuck with arbitrary choses enforced by the compiler
P: Flow → Service type
Network controller
Routing
Failure recovery
QoS
Elasticity
Load balancing

---
An SDN research perspective
What are the right abstractions for the Northbound interface?
SDN app
SDN app
Abstraction
SDN app
Policy languages
(FatTire, FlowTags, FML, E2)
Northbound
interface
SDN controller
Southbound
interface
(OpenFlow)
Modular flowtable languages
(NetKAT, Pyretic)
Flowtable languages
(OpenFlow, P4)
Flexibility

---
Correct-by-construction networking
- Flexibility vs abstraction: can you have your cake and eat it too?
- Yes, you just need two cakes
Abstraction
Flexibility
Correct-by-construction networking
Spec0: Network policy
refinement
refinement
Spec1
Spec2
SpecN
Abstraction
Flexibility

---
Correct-by-construction networking
Spec0: Network policy
refinement
refinement
Spec1
Spec2
SpecN
- Refinements deal with network topology, routing, fault tolerance, load balancing, etc.
- Each refinement focuses on a fragment of the network
- Each refinement is simple enough to verify automatically
- The final specification describes each network component in detail and can be compiled directly into an SDN controller
- Correctness of each refinement guarantees that the final spec satisfies the high-level policy

---
Thank You!