TOWARDS CORRECT-BY-CONSTRUCTION SDN
Leonid Ryzhyk Nikolaj Bjorner Marco Canini Jean-Baptiste Jeannin Nina Narodytska
Cole Schlesinger Douglas Terry George Varghese
22 August 2016

---
INTRODUCTION
- Cocoon is a
  - high-level SDN programming language
  - SDN programming methodology
  - verification tool
- … based on the principle of correctness by construction

---
COCOON IN A NUTSHELL
Traditional SDN Verification Workflow
Design
Implement
Run on the
controller
Verify generated
network configuration
SDN verification with Cocoon
refine
refine
refine
spec
implementation
Correct by construction

---
EXAMPLE: CAMPUS NETWORK
[Sung et al. Towards Systematic Design of Enterprise Networks]
L2 segment
Router
VLAN Gateway
Switch

---
INTER-VLAN ROUTING: HOP1

---
INTER-VLAN ROUTING: HOP2

---
INTER-VLAN ROUTING: HOP3
This is messy:
Large, ad hoc topology
L2/L3 routing are mixed up
Complex security policies
Typical bugs:
ACL distribution
Routing loops
Black holes
Let’s try to untangle this design …

---
STEP 1: HIGH-LEVEL SPECIFICATION

---
STEP 2: DISTRIBUTED ACLs

---
STEP 2: DISTRIBUTED ACLs
Assumption: acl() ≡ aclOut() Λ aclIn()

---
STEP 3: L3 ROUTING

---
STEP 3: L3 ROUTING
Assumption: l3NextHop(GatewayIP)* = Gateway

---
STEP 4: L2 SWITCHING

---
STEP 4: L2 SWITCHING

---
STEP 4: L2 SWITCHING
Assumption: l2NextHop(vlan)* = l3NextHop(vlan)

---
STEP 4: L2 SWITCHING
l2NextHop(vlan=0)
l2NextHop(vlan=green)
l2NextHop(vlan=red)
l2NextHop(vlan=blue)

---
SEPARATION OF CONCERNS
High-level spec
Distributed access control
L3 routing
L2 switching

---
WOULDN’T IT BE GREAT TO BUILD SDNs
THIS WAY?
With Cocoon, you can!
Language support for refinement-based programming
Automatic compositional verification
Parameterized specifications
Spec may contain undefined functions, e.g., acl(), l2NextHop()
Verification relies on assumptions
Assumptions are validated when concrete definitions are provided (statically or at runtime)
The Cocoon compiler supports P4 and OpenFlow (via NetKAT) backends

---
CASE STUDIES
Campus network
[Sung et al. Towards Systematic Design of Enterprise Networks]
F10
[Liu et al. F10: A Fault-Tolerant Engineered Network]
B4-style WAN
[Jain et al. B4: Experience with a Globally-Deployed Software Defined WAN]
iSDX (Software-defined Internet Exchange)
[Gupta et al. An Industrial-Scale Software Defined Internet Exchange Point]
NSX-style network virtualization framework
[Koponen et al. Network Virtualization in Multi-tenant Datacenters]
Stag (source-based routing + security labels for fat-tree topology)

---
PERFORMANCE
All case studies verified

---
CORRECTNESS GUARANTEES

---
PROPERTY-BASED VERIFICATION IN COCOON